## Slide 1: Computer Organization
Computer Organization - It tells us how exactly all the units in the system are arranged and interconnected.
deals with components of a connection in a system.
Computer Architecture – It helps us to understand the functionalities of a system.

## Slide 2: Basic Organization of a Computer

## Slide 3
Input Unit
Output Unit
Central Processing Unit (CPU)
Control Unit (CU)
Arithmetic And Logic Unit (ALU)
Memory Unit - (i)Primary memory (ii)Secondary memory

## Slide 4: Example
Instruction Cycle

## Slide 5
CSE 211, Computer Organization and Architecture
Overview
Instruction Codes
Computer Registers
Computer Instructions
Common Bus System
Timing and Control
Instruction Cycle
Memory Reference Instructions
Input-Output and Interrupt
Complete Computer Description

## Slide 6
Instruction Codes
Instruction codes are groups of bits that tell the computer to perform a specific task.
Operation Code (Opcode): Specifies the operation to be performed, such as addition, subtraction, or shifting.
Address/Operand Part: Specifies where the data (operands) for the operation is located, either in a register or a memory address.
Addressing Modes: A mode bit distinguishes between direct addressing (data is at the specified address)
And indirect addressing (the specified address contains another address for the data).

## Slide 7
Introduction
Every different processor type has its own design (different registers, buses, microoperations, machine instructions, etc)
Modern processor is a very complex device
It contains
  Many registers
  Multiple arithmetic units, for both integer and floating point calculations
  The ability to pipeline several consecutive instructions to speed execution
  Etc.
However, to understand how processors work, we will start with a simplified processor model

## Slide 8
Basic Computer
The Basic Computer has two components, a processor and memory
The memory has 4096 words in it
  4096 = 212, so it takes 12 bits to select a word in memory
Each word is 16 bits long
CPU
RAM
0
4095
0
15

## Slide 9
CSE 211, Computer Organization and Architecture
Instruction
Program
  A sequence of (machine) instructions
(Machine) Instruction
  A group of bits that tell the computer to perform a specific operation (a sequence of micro-operation)
The instructions of a program, along with any needed data are stored in memory

## Slide 10
CSE 211, Computer Organization and Architecture
Instruction
The CPU reads the next instruction from memory
It is placed in an Instruction Register (IR)
Control circuitry in control unit then translates the instruction into the sequence of microoperations
It is very necessary to implement it

## Slide 11
Instruction Codes
Instruction codes are groups of bits that tell the computer to perform a specific task.
Operation Code (Opcode): Specifies the operation to be performed, such as addition, subtraction, or shifting.
Address/Operand Part: Specifies where the data (operands) for the operation is located, either in a register or a memory address.
Addressing Modes: A mode bit distinguishes between direct addressing (data is at the specified address)
And indirect addressing (the specified address contains another address for the data).

## Slide 12
CSE 211, Computer Organization and Architecture
Instruction Format
A computer instruction is often divided into two parts
  An opcode (Operation Code) that specifies the operation for that instruction
  An address that specifies the registers and/or locations in memory to use for that operation
In the Basic Computer, since the memory contains 4096 (= 212) words,
we needs 12 bit to specify which memory address this instruction will use
Opcode
Address
Instruction Format
15
14
12
0
I
11
Addressing
mode

## Slide 13
CSE 211, Computer Organization and Architecture
Instruction Format
In the Basic Computer,
  15 bit of the instruction specifies the addressing mode
  (0: direct addressing, 1: indirect addressing)
Since the memory words, and hence the instructions, are 16 bits long, that leaves 3 bits for the instruction’s opcode
Opcode
Address
Instruction Format
15
14
12
0
I
11
Addressing
mode

## Slide 14
CSE 211, Computer Organization and Architecture
Addressing Mode
The address field of an instruction can represent either
  Direct address: the address in memory of the data to use (the address of the operand), or
  Indirect address: the address in memory of the address in memory of the data to use
Effective Address (EA)
  The address, that can be directly used without modification to access an operand for a computation-type instruction, or as the target address for a branch-type instruction
0
ADD
457
22
Operand
457
1
ADD
300
35
1350
300
Operand
1350
+
AC
+
AC
Direct addressing
Indirect addressing

## Slide 15
CSE 211, Computer Organization and Architecture
Processor Register
A processor has many registers to hold instructions, addresses, data, etc
The processor has a register, the Program Counter (PC) that holds the memory address of the next instruction to get
Since the memory in the Basic Computer only has 4096 locations, the PC only needs 12 bits

## Slide 16
CSE 211, Computer Organization and Architecture
Processor Register
In a direct or indirect addressing, the processor needs to keep track of what locations in memory it is addressing:
  The Address Register (AR) is used for this
  The AR is a 12 bit register in the Basic Computer
When an operand is found, using either direct or indirect addressing, it is placed in the Data Register (DR).
  The processor then uses this value as data for its operation
The Basic Computer has a single general purpose register – the Accumulator (AC)

## Slide 17
CSE 211, Computer Organization and Architecture
Processor Register
The significance of a general purpose register is that it can be referred to in instructions
  e.g. load AC with the contents of a specific memory location; store the contents of AC into a specified memory location
Often a processor will need a scratch register to store intermediate results or other temporary data;
  in the Basic Computer this is the Temporary Register (TR)

## Slide 18
CSE 211, Computer Organization and Architecture
Processor Register
The Basic Computer uses a very simple model of input/output (I/O) operations
  Input devices are considered to send 8 bits of character data to the processor
  The processor can send 8 bits of character data to output devices
The Input Register (INPR) holds an 8 bit character gotten from an input device
The Output Register (OUTR) holds an 8 bit character to be send to an output device

## Slide 21
CSE 211, Computer Organization and Architecture
Processor Register
List of BC Registers
  DR 16 Data Register Holds memory operand
  AR 12 Address Register Holds address for memory
  AC 16 Accumulator Processor register
  IR 16 Instruction Register Holds instruction code
  PC 12 Program Counter Holds address of instruction
  TR 16 Temporary Register Holds temporary data
  INPR 8 Input Register Holds input character
  OUTR 8 Output Register Holds output character
Registers in the Basic Computer
11
0
PC
15
0
IR
15
0
TR
7
0
OUTR
15
0
DR
15
0
AC
11
0
AR
INPR
0
7
Memory
4096 x 16
CPU

## Slide 22
CSE 211, Computer Organization and Architecture
Common Bus System
The registers in the Basic Computer are connected using a bus
This gives a savings in circuitry over complete connections between registers

## Slide 23
CSE 211, Computer Organization and Architecture
Common Bus System
S1
S0
Bus
Memory unit
4096 x 16
LD INR CLR
Address
Read
Write
AR
LD INR CLR
PC
LD INR CLR
DR
LD INR CLR
AC
ALU
E
INPR
IR
LD
LD INR CLR
TR
OUTR
LD
Clock
7
1
2
3
4
5
6

## Slide 24
CSE 211, Computer Organization and Architecture
Common Bus System
Three control lines, S2, S1, and S0 control which register the bus selects as its input
Either one of the registers will have its load signal activated, or the memory will have its read signal activated
  Will determine where the data from the bus gets loaded
0 0 0 x
0 0 1 AR
0 1 0 PC
0 1 1 DR
1 0 0 AC
1 0 1 IR
1 1 0 TR
1 1 1 Memory
S2 S1 S0 Register

## Slide 25
CSE 211, Computer Organization and Architecture
Common Bus System
Either one of the registers will have its load signal activated, or the memory will have its read signal activated
  Will determine where the data from the bus gets loaded
The 12-bit registers, AR and PC, have 0’s loaded onto the bus in the high order 4 bit positions
When the 8-bit register OUTR is loaded from the bus, the data comes from the low order 8 bits on the bus

## Slide 26
CSE 211, Computer Organization and Architecture
Basic Computer Instructions
Basic Computer Instruction Format
15 14
12 11
0
I
Opcode
Address
1. Memory-Reference Instructions (OP-code = 000 ~ 110)
2. Register-Reference Instructions (OP-code = 111, I = 0)
3. Input-Output Instructions (OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 27
CSE 211, Computer Organization and Architecture
Basic Computer Instructions
  AND 0xxx 8xxx AND memory word to AC
  ADD 1xxx 9xxx Add memory word to AC
  LDA 2xxx Axxx Load AC from memory
  STA 3xxx Bxxx Store content of AC into memory
  BUN 4xxx Cxxx Branch unconditionally
  BSA 5xxx Dxxx Branch and save return address
  ISZ 6xxx Exxx Increment and skip if zero
  CLA 7800 Clear AC
  CLE 7400 Clear E
  CMA 7200 Complement AC
  CME 7100 Complement E
  CIR 7080 Circulate right AC and E
  CIL 7040 Circulate left AC and E
  INC 7020 Increment AC
  SPA 7010 Skip next instr. if AC is positive
  SNA 7008 Skip next instr. if AC is negative
  SZA 7004 Skip next instr. if AC is zero
  SZE 7002 Skip next instr. if E is zero
  HLT 7001 Halt computer
  INP F800 Input character to AC
  OUT F400 Output character from AC
  SKI F200 Skip on input flag
  SKO F100 Skip on output flag
  ION F080 Interrupt on
  IOF F040 Interrupt off
Hex Code
Symbol I = 0 I = 1 Description

## Slide 28
CSE 211, Computer Organization and Architecture
Instruction Set Completeness
Instruction Types
A computer should have a set of instructions so that the user can construct machine language programs to evaluate any function that is known to be computable.
  Functional Instructions
  - Arithmetic, logic, and shift instructions
  - ADD, CMA, INC, CIR, CIL, AND, CLA
  Transfer Instructions
  - Data transfers between the main memory and the processor registers
  - LDA, STA
  Control Instructions
  - Program sequencing and control
  - BUN, BSA, ISZ
  Input/output Instructions
  - Input and output
  - INP, OUT

## Slide 29
CSE 211, Computer Organization and Architecture
Control Unit
Control unit (CU) of a processor translates from machine instructions to the control signals for the microoperations that implement them
Control units are implemented in one of two ways
Hardwired Control
  CU is made up of sequential and combinational circuits to generate the control signals
Microprogrammed Control
  A control memory on the processor contains microprograms that activate the necessary control signals
We will consider a hardwired implementation of the control unit for the Basic Computer

## Slide 30
CSE 211, Computer Organization and Architecture
Timing and Control
Control unit of Basic Computer
Instruction register (IR)
15
14 13 12
11 - 0
3 x 8
decoder
7 6 5 4 3 2 1 0
I
D
0
15 14 . . . . 2 1 0
4 x 16
decoder
4-bit
sequence
counter
(SC)
Increment (INR)
Clear (CLR)
Clock
Other inputs
Control
signals
D
T
T
7
15
0
Combinational
Control
logic

## Slide 31
CSE 211, Computer Organization and Architecture
Timing Signals
- Generated by 4-bit sequence counter and 416 decoder
- The SC can be incremented or cleared.
- Example: T0, T1, T2, T3, T4, T0, T1, . . .
Assume: At time T4, SC is cleared to 0 if decoder output D3 is active.
D3T4: SC  0

## Slide 32
CSE 211, Computer Organization and Architecture
Instruction Cycle
In Basic Computer, a machine instruction is executed in the following cycle:
  Fetch an instruction from memory
  Decode the instruction
  Read the effective address from memory if the instruction has an indirect address
  Execute the instruction
After an instruction is executed, the cycle starts again at step 1, for the next instruction
Note: Every different processor has its own (different) instruction cycle

## Slide 33
CSE 211, Computer Organization and Architecture
Fetch and Decode
Fetch and Decode
T0: AR PC (S0S1S2=010, T0=1)
T1: IR  M [AR], PC  PC + 1 (S0S1S2=111, T1=1)
T2: D0, . . . , D7  Decode IR(12-14), AR  IR(0-11), I  IR(15)
S2
S1
S0
Bus
7
Memory
unit
Address
Read
AR
LD
PC
INR
IR
LD
Clock
1
2
5
Common bus
T1
T0

## Slide 34
CSE 211, Computer Organization and Architecture
Flow Chart (Instruction Cycle)
= 0 (direct)
Start
SC <-- 0
AR
<--
PC
T0
IR
<--
M[AR],
PC
<--
PC + 1
T1
AR
<--
IR(0-11),
I
<--
IR(15)
Decode Opcode in IR(12-14),
T2
D7
= 0 (Memory-reference)
(Register or I/O) = 1
I
I
Execute
register-reference
instruction
SC
<--
0
Execute
input-output
instruction
SC
<--
0
M[AR]
<--
AR
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute
memory-reference
instruction
SC
<--
0
T4

## Slide 35
CSE 211, Computer Organization and Architecture
Determining Type of Instruction
D'7IT3: AR M[AR]
D'7I'T3: Nothing
D7I'T3: Execute a register-reference instr.
D7IT3: Execute an input-output instr.

## Slide 36
CSE 211, Computer Organization and Architecture
Register Reference Instruction
r = D7 IT3 => Register Reference Instruction
Bi = IR(i) , i=0,1,2,...,11
- D7 = 1, I = 0
- Register Ref. Instr. is specified in b0 ~ b11 of IR
- Execution starts with timing signal T3
Register Reference Instructions are identified when
r: SC  0
CLA rB11: AC  0
CLE rB10: E  0
CMA rB9: AC  AC’
CME rB8: E  E’
CIR rB7: AC  shr AC, AC(15)  E, E  AC(0)
CIL rB6: AC  shl AC, AC(0)  E, E  AC(15)
INC rB5: AC  AC + 1
SPA rB4: if (AC(15) = 0) then (PC  PC+1)
SNA rB3: if (AC(15) = 1) then (PC  PC+1)
SZA rB2: if (AC = 0) then (PC  PC+1)
SZE rB1: if (E = 0) then (PC  PC+1)
HLT rB0: S  0 (S is a start-stop flip-flop)

## Slide 37
CSE 211, Computer Organization and Architecture
Memory Reference Instructions
AND to AC
D0T4: DR  M[AR] Read operand
D0T5: AC  AC  DR, SC  0 AND with AC
ADD to AC
D1T4: DR  M[AR] Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 Add to AC and store carry in E
- The effective address of the instruction is in AR and was placed there during
timing signal T2 when I = 0, or during timing signal T3 when I = 1
- Memory cycle is assumed to be short enough to complete in a CPU cycle
- The execution of MR instruction starts with T4
Symbol
Operation
Decoder
Symbolic Description
AND D0 AC  AC  M[AR]
ADD D1 AC  AC + M[AR], E  Cout
LDA D2 AC  M[AR]
STA D3 M[AR]  AC
BUN D4 PC  AR
BSA D5 M[AR]  PC, PC  AR + 1
ISZ D6 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1

## Slide 38
CSE 211, Computer Organization and Architecture
Memory Reference Instructions
Memory, PC after execution
21
0
BSA
135
Next instruction
Subroutine
20
PC = 21
AR = 135
136
1
BUN
135
Memory, PC, AR at time T4
0
BSA
135
Next instruction
Subroutine
20
21
135
PC = 136
1
BUN
135
LDA: Load to AC
D2T4: DR  M[AR]
D2T5: AC  DR, SC  0
STA: Store AC
D3T4: M[AR]  AC, SC  0
BUN: Branch Unconditionally
D4T4: PC  AR, SC  0
BSA: Branch and Save Return Address
M[AR]  PC, PC  AR + 1

## Slide 39
CSE 211, Computer Organization and Architecture
Memory Reference Instructions
BSA:
D5T4: M[AR]  PC, AR  AR + 1
D5T5: PC  AR, SC  0
ISZ: Increment and Skip-if-Zero
D6T4: DR  M[AR]
D6T5: DR  DR + 1
D6T4: M[AR]  DR, if (DR = 0) then (PC  PC + 1), SC  0

## Slide 40
CSE 211, Computer Organization and Architecture
Flow Chart - Memory Reference Instructions
Memory-reference instruction
DR  M[AR]
DR  M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC DR
SC  0
AC  AC + DR
E  Cout
SC  0
AC  DR
SC  0
D T
0
4
D T
1
4
D T
2
4
D T
3
4
D T
0
5
D T
1
5
D T
2
5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D T
4
4
D T
5
4
D T
6
4
DR  DR + 1
D T
5
5
D T
6
5
PC  AR
SC  0
M[AR]  DR
If (DR = 0)
then (PC  PC + 1)
SC  0
D T
6
6


## Slide 41
CSE 211, Computer Organization and Architecture
Input/Output and Interrupt
Input-Output Configuration
INPR Input register - 8 bits
OUTR Output register - 8 bits
FGI Input flag - 1 bit
FGO Output flag - 1 bit
IEN Interrupt enable - 1 bit
A Terminal with a keyboard and a Printer
Input-output
terminal
Serial
communication
interface
Computer
registers and
flip-flops
Printer
Keyboard
Receiver
interface
Transmitter
interface
FGO
OUTR
AC
INPR
FGI
Serial Communications Path
Parallel Communications Path

## Slide 42
CSE 211, Computer Organization and Architecture
Input/Output and Interrupt
Transmisson Process -
- The terminal sends and receives serial information
- The serial info. from the keyboard is shifted into INPR
- The serial info. for the printer is stored in the OUTR
- INPR and OUTR communicate with the terminal serially and with the AC in parallel.
- The flags are needed to synchronize the timing difference between I/O device and the computer
A Terminal with a keyboard and a Printer

## Slide 43
CSE 211, Computer Organization and Architecture
Input/Output Instructions
D7IT3 = p
IR(i) = Bi, i = 6, …, 11
p: SC  0 Clear SC
INP pB11: AC(0-7)  INPR, FGI  0 Input char. to AC
OUT pB10: OUTR  AC(0-7), FGO  0 Output char. from AC
SKI pB9: if(FGI = 1) then (PC  PC + 1) Skip on input flag
SKO pB8: if(FGO = 1) then (PC  PC + 1) Skip on output flag
ION pB7: IEN  1 Interrupt enable on
IOF pB6: IEN  0 Interrupt enable off

## Slide 44
CSE 211, Computer Organization and Architecture
Interrupt Initiated Input/Output
- Open communication only when some data has to be passed --> interrupt.
- The I/O interface, instead of the CPU, monitors the I/O device.
- When the interface founds that the I/O device is ready for data transfer,
it generates an interrupt request to the CPU

## Slide 45
CSE 211, Computer Organization and Architecture
Interrupt Initiated Input/Output
- Upon detecting an interrupt, the CPU stops momentarily the task
it is doing, branches to the service routine to process the data
transfer, and then returns to the task it was performing.
FGI – 1 new info. Is available to input device……0 info accepted by computer
FGO – 1 info tranffered from AC to OUTR………0 don’t load new things
IEN (Interrupt-enable flip-flop)
- can be set and cleared by instructions
- when cleared, the computer cannot be interrupted

## Slide 46
CSE 211, Computer Organization and Architecture
Flow Chart of Interrupt Cycle
R = Interrupt f/f
- The interrupt cycle is a HW implementation of a branch and save return address operation.
- At the beginning of the next instruction cycle, the instruction that is read from memory is in address 1.
- At memory address 1, the programmer must store a branch instruction that sends the control to an interrupt service routine
- The instruction that returns the control to the original program is "indirect BUN 0"
Store return address
R
=1
=0
in location 0
M[0]  PC
Branch to location 1
PC  1
IEN  0
R  0
Interrupt cycle
Instruction cycle
Fetch and decode
instructions
IEN
FGI
FGO
Execute
instructions
R  1
=1
=1
=1
=0
=0
=0
INPR Input register - 8 bits
OUTR Output register - 8 bits
FGI Input flag - 1 bit
FGO Output flag - 1 bit
IEN Interrupt enable - 1 bit

## Slide 47
CSE 211, Computer Organization and Architecture
Register Transfer Operations in Interrupt Cycle
Register Transfer Statements for Interrupt Cycle
- R F/F  1 if IEN (FGI + FGO)T0T1T2
 T0T1T2 (IEN)(FGI + FGO): R  1
- The fetch and decode phases of the instruction cycle
must be modified Replace T0, T1, T2 with R'T0, R'T1, R'T2
- The interrupt cycle :
RT0: AR  0, TR  PC
RT1: M[AR]  TR, PC  0
RT2: PC  PC + 1, IEN  0, R  0, SC  0
After interrupt cycle
0
BUN
1120
0
1
PC = 256
255
1
BUN
0
Before interrupt
Main
Program
1120
I/O
Program
0
BUN
1120
0
PC = 1
256
255
1
BUN
0
Memory
Main
Program
1120
I/O
Program
256

## Slide 48
CSE 211, Computer Organization and Architecture
Complete Computer Design
=1 (I/O) =0 (Register) =1(Indir) =0(Dir)
start
SC  0, IEN  0, R  0
R
AR  PC
R’T0
IR  M[AR], PC  PC + 1
R’T1
AR  IR(0~11), I  IR(15)
D0...D7  Decode IR(12 ~ 14)
R’T2
AR  0, TR  PC
RT0
M[AR]  TR, PC  0
RT1
PC  PC + 1, IEN  0
R  0, SC  0
RT2
D7
I
I
Execute
I/O
Instruction
Execute
RR
Instruction
AR <- M[AR]
Idle
D7IT3 D7I’T3
D7’IT3 D7’I’T3
Execute MR
Instruction
=0(Instruction =1(Interrupt
Cycle) Cycle)
=1(Register or I/O) =0(Memory Ref)
D7’T4
INPR Input register - 8 bits
OUTR Output register - 8 bits
FGI Input flag - 1 bit
FGO Output flag - 1 bit
IEN Interrupt enable - 1 bit

## Slide 49
CSE 211, Computer Organization and Architecture
Complete Computer Design
Fetch
Decode
Indirect
Interrupt
Memory-Reference
AND
ADD
LDA
STA
BUN
BSA
ISZ
RT0:
RT1:
RT2:
D7IT3:
RT0:
RT1:
RT2:
D0T4:
D0T5:
D1T4:
D1T5:
D2T4:
D2T5:
D3T4:
D4T4:
D5T4:
D5T5:
D6T4:
D6T5:
D6T6:
AR  PC
IR  M[AR], PC  PC + 1
D0, ..., D7  Decode IR(12 ~ 14),
AR  IR(0 ~ 11), I  IR(15)
AR  M[AR]
R  1
AR  0, TR  PC
M[AR]  TR, PC  0
PC  PC + 1, IEN  0, R  0, SC  0
DR  M[AR]
AC  AC  DR, SC  0
DR  M[AR]
AC  AC + DR, E  Cout, SC  0
DR  M[AR]
AC  DR, SC  0
M[AR]  AC, SC  0
PC  AR, SC  0
M[AR]  PC, AR  AR + 1
PC  AR, SC  0
DR  M[AR]
DR  DR + 1
M[AR]  DR, if(DR=0) then (PC  PC + 1),
SC  0

## Slide 50
CSE 211, Computer Organization and Architecture
Complete Computer Design
Register-Reference
CLA
CLE
CMA
CME
CIR
CIL
INC
SPA
SNA
SZA
SZE
HLT
Input-Output
INP
OUT
SKI
SKO
ION
IOF
D7IT3 = r
IR(i) = Bi
r:
rB11:
rB10:
rB9:
rB8:
rB7:
rB6:
rB5:
rB4:
rB3:
rB2:
rB1:
rB0:
D7IT3 = p
IR(i) = Bi
p:
pB11:
pB10:
pB9:
pB8:
pB7:
pB6:
(Common to all register-reference instr)
(i = 0,1,2, ..., 11)
SC  0
AC  0
E  0
AC  AC
E  E
AC  shr AC, AC(15)  E, E  AC(0)
AC  shl AC, AC(0)  E, E  AC(15)
AC  AC + 1
If(AC(15) =0) then (PC  PC + 1)
If(AC(15) =1) then (PC  PC + 1)
If(AC = 0) then (PC  PC + 1)
If(E=0) then (PC  PC + 1)
S  0
(Common to all input-output instructions)
(i = 6,7,8,9,10,11)
SC  0
AC(0-7)  INPR, FGI  0
OUTR  AC(0-7), FGO  0
If(FGI=1) then (PC  PC + 1)
If(FGO=1) then (PC  PC + 1)
IEN  1
IEN  0

## Slide 51
CSE 211, Computer Organization and Architecture
Design of a Basic Computer(BC)
Hardware Components of BC
A memory unit: 4096 x 16.
Registers:
AR, PC, DR, AC, IR, TR, OUTR, INPR, and SC
Flip-Flops(Status):
I, S, E, R, IEN, FGI, and FGO
Decoders: a 3x8 Opcode decoder
a 4x16 timing decoder
Common bus: 16 bits
Control logic gates:
Adder and Logic circuit: Connected to AC
Control Logic Gates
  - Input Controls of the nine registers
  - Read and Write Controls of memory
  - Set, Clear, or Complement Controls of the flip-flops
  - S2, S1, S0 Controls to select a register for the bus
  - AC, and Adder and Logic circuit